## Slide 1: Dancing Monkeys: Accelerated
GPU-Accelerated Beat Detection for Dancing Monkeys
Philip Peng, Yanjie Feng
UPenn CIS 565 Spring 2012
Final Project – Midpoint Presentation
img src: http://www.dcrblogs.com/wp-content/uploads/2010/03/radioactive-dancing-monkeys-fastest-ani.gif

## Slide 2: Project Description
Dancing Monkeys
  Create DDR step patterns from arbitrary songs
  Highly precise beat detection algorithm (accurate within <0.0001 BPM)
  Nov 1, 2003 by Karl O’Keeffe
  MATLAB program, CC license
  http://monket.net/dancing-monkeys-v2/
GPU Acceleration
  Algorithm used = brute force BPM comparisons
  GPUs are good with parallel number crunching!
img src: http://monket.net/uploaded-v2/Feet.png

## Slide 3: Dancing Monkeys Architecture
Process waveform data
Calculate BPM (first pass)
Calculate BPM (second pass)
Calculate gap time
Generate arrow patterns from waveform data

## Slide 4: Timing Breakdown
Process | Time (s)
timeProgram | 202.748426
timeArgs | 0.082273
timeSong | 202.651163
timePrep | 9.432683
timeInfo | 7.371580
timeData | 1.797109
timePeaks | 0.253459
timeBpm1 | 185.960192
timeTest | 126.409699
timeTestTop | 0.002460
timeFit | 59.377492
timeFitBest | 0.154692
Process | Time (s)
timeBpm2 | 1.200393
timeTest | 1.184987
timeTestTop | 0.000064
timeFit | 0.000122
timeFitBest | 0.006139
timeGap | 1.663195
timeEnergy | 0.040256
timeSimilar | 1.617153
timeGenerate | 4.375886
timeCliques | 0.035418
timePause | 0.431286
timeArrow | 0.350256
timeOutput | 3.546520

## Slide 5: Timing Breakdown
Chart: timeSong Breakdown
| timePrep | timeBpm1 | timeBpm2 | timeGap | timeGenerate
Comparison of Time Spent | 9.4327 | 185.9602 | 1.2004 | 1.6632 | 4.3759
Chart: timeBpm Breakdown
| timeTest | timeTestTop | timeFit | timeFitBest
timeBpm1 Breakdown | 126.4097 | 0.00246 | 59.3775 | 0.15469

## Slide 6: Code Analysis
timeBPM (first pass) longest: brute force BPM comparisons
  BPM [89, 205], Frequency = 44100
  Interval = round(Frequency / (BPM / 60));
  Interval = [12907, 29730], IntervalFrequency = 10
  Total of 1682 loops

## Slide 7: CPU Parallelization - Approach
MATLAB’s Parallel Computing Toolbox
Replace for loops with MATLAB’s parfor
  Run loop in parallel, one per CPU core
  http://www.mathworks.com/help/toolbox/distcomp/parfor.html
Require code modification
  matlabpool
  Temporary arrays
  Index recalculations

## Slide 8: CPU Parallelization - Code

## Slide 9: CPU Parallelization - Results
Chart: 
| timeTest | timeFit | timeBpm | timeProgram
base | 126.4097 | 59.3775 | 185.9602 | 202.7484
parfor | 47.2064 | 30.4471 | 77.6756 | 93.3126
 | base | parfor | %
timeTest | 126.4 | 47.2 | 37.5%
timeFit | 59.3 | 30.4 | 51.3%
timeBpm | 186.0 | 77.7 | 41.8%
timeProgram | 202.7 | 93.3 | 46.0%

## Slide 10: GPU Parallelization - Approach
TODO
http://www.mathworks.com/help/toolbox/distcomp/bsic3by.html

## Slide 11: GPU Parallelization - Issues
TODO
Global variables/data structures
Rewrite code
Slow memory copy

## Slide 12: Questions?
Blog: http://dancingmonkeysaccelerated.blogspot.com/
Code: https://github.com/Keripo/DancingMonkeysAccelerated
img src: http://www.gratuitousscience.com/wp-content/uploads/2010/04/6a00d83451f25369e200e54f94996e8834-800wi.jpg